## Slide 1: Introduction to Reconfigurable Computing Introduction to the development kits and design software
Lecture 1
Iouliia Skliarova

## Slide 2: Reconfigurable Computing
A computer architecture that facilitates faster and more complex computing by using reprogrammable integrated circuits to process data that solves problems and directs specified functions.
Offers the higher speed and efficiency of computer hardware to perform serial and parallel tasks combined with software’s flexible capacity to allow changes to a circuit’s purpose in the field to adjust for changing circumstances.
Core advantages:
  More functionality from simpler and smaller hardware designs
  Cost savings on low volume products and those whose useful life is extended by updating
  Shorter/faster development time-to-market

## Slide 3
The earliest work on reconfigurable computer architecture was done at the University of California at Los Angeles – in 1960’s Gerald Estrin proposed a standard processor extended with an array of “variable” hardware.
The main goal was to permit computations which are beyond the capabilities of present systems by providing an inventory of high speed substructures and rules for interconnecting them such that the entire system may be temporarily distorted into a problem oriented special purpose computer.
At that time, digital technology was not ready for such a revolutionary change.
Original Idea

## Slide 4: Other Computing Models
Traditionally, computing was classified into General-Purpose Computing performed by a General-Purpose Processor (GPP) and Application-Specific Computing performed by an Application-Specific Integrated Circuit (ASIC).
Reconfigurable computing acts as a trade-off between the two extreme characteristics of GPP and ASIC, combining the advantages of both.
When compared to GPP:
  provides ability to make substantial changes to the datapath itself in addition to the control flow
  can have better performance with respect to a software implementation in GPP but paying this in terms of time to implement
When compared to ASIC:
  possibility to adapt the hardware <during runtime> by "loading" a new circuit on the reconfigurable fabric
  can be used to design a system without requiring the same design time and complexity compared to a full custom solution but being beaten in terms of performance

## Slide 5: Overview
Advantages / Features
  Flexible hardware/software co-design
  Customization (parallelism exploration, specialized control and datapaths)
  Fast prototyping
  Faster design cycles, lower risk, cheaper for small to medium size markets compared with ASICs
  Dynamic system upgrades (field updates for both hardware and software)
Target applications
  Application-specific hardware accelerators/coprocessors/processors
  Telecommunications, networks, image/audio processing, cryptography, space, automotive, medical, etc.

## Slide 6: Overview
Limitations
  Overhead due to reconfiguration time and/or additional hardware circuit delays
Supporting technologies
  High capacity FPGAs/Programmable SoC
  Processor customization frameworks
    Fixed processor cores + extension coprocessors / flexible processors
Reconfiguration approaches
  Static (at manufacturing, deployment or boot time)
  Dynamic
    Total (at run-time between execution phases)
    Partial (at runtime replacing some components, while others remain operational)

## Slide 7: FPGA – Field-Programmable Gate Array

## Slide 8: Modern FPGA
6-input LUTs configurable as distributed memory
Embedded memory blocks - block RAM with built-in FIFO logic for on-chip data buffering
High-speed serial connectivity with built-in multi-gigabit transceivers
User configurable analog interfaces, incorporating analog-to-digital converters
DSP slices with dedicated multipliers for high-performance filtering
Clock management tiles providing clock frequency synthesis, deskew, and jitter filtering functionality
Soft and hard processors
  => FPGAs with hard processor cores are referred to as programmable systems-on-chip (PSoC)
The simplest FPGAs contain only programmable fabric and configurable general purpose IO (GPIO) (a); different architectures augment this fundamental fabric with memory blocks, PLLs, and clock managers (b); DSP blocks and SERDES interfaces (c); and hard processor cores and peripherals (d). (Image source: Max Maxfield)

## Slide 9: Xilinx Programmable Devices
The performance and capabilities of the programmable device offerings from Xilinx span from modest to extremely high:
  traditional FPGAs
  PSoCs (FPGA programmable fabric with a single hard core processor)
  MPSoCs (FPGA programmable fabric with a multiple hard core processors)
  RFSoCs (MPSoCs with RF capability)
  ACAPs (Adaptive Compute Acceleration Platforms)

## Slide 10: Xilinx FPGA

## Slide 11: Artix-7 CLB (Configurable Logic Block)
CLBs are the main logic resources for implementing sequential as well as combinatorial circuits.
Each CLB element is connected to a switch matrix for access to the general routing matrix.
A CLB element contains a pair of slices.
Every slice contains:
  Four logic-function generators (or look-up tables)
  Eight storage elements
  Wide-function multiplexers
  Carry logic

## Slide 12: Nexys-4 Development Board
  16 user switches
  16 user LEDs
  Two 4-digit 7-segment displays
  USB-UART Bridge
  Two tri-color LEDs
  Micro SD card connector
  12-bit VGA output
  PWM audio output
  PDM microphone
  3-axis accelerometer
  Temperature sensor
  10/100 Ethernet PHY
  16MB CellularRAM
  Serial Flash
  Four Pmod ports
  Pmod for XADC signals
  Digilent USB-JTAG port for FPGA programming and communication
  USB HID Host for mice, keyboards and memory sticks
FPGA: xc7a100Tcsg324-1

## Slide 13: Nexys-4 Development Board
USB cable for power supply and programming
Power switch
Programming mode jumper: USB/SD
External configuration jumper (SD / USB): USB
Power select jumper: USB

## Slide 14: Development Tools
Xilinx Vitis
  For portability of projects between different computers, it is recommended to install version 2020.2
  Installation instructions are available at the course website
  Requires at least 70 GB of disk space
  License: Vivado Design Suite 30-day evaluation license -> floating license available within the UA campus or with active VPN

## Slide 15: FPGA Design Flow
Design entry based on:
  Hardware description languages
  State diagrams
  Schematic capture
  C/C++ and other high level languages

## Slide 16: Logic Synthesis
Results in a netlist (i.e. hardware components and their interconnections) that implement the modeled behavior and structure
Outputs
  Netlist
  Circuit performance and resource usage estimations

## Slide 17: Implementation (Map, Place and Route)
Maps the netlist in FPGA primitives
Places the primitives in specific FPGA locations
Routes the interconnections between primitives
Outputs
  FPGA configuration file
  Reports with FPGA resource usage, circuit delays, power consumption, …

## Slide 18: Device (FPGA) Programming
Transfers the configuration file to the FPGA
  Done with a software tool and a programming cable
  Most FPGAs are based on SRAM (volatile configuration)
  Some devices are based on non volatile FLASH memory

## Slide 19: System-on-Chip (SoC)
A SoC is a single integrated circuit integrating at least components like a processor and I/O peripherals to perform general user interface and housekeeping tasks and special hardware accelerators to handle computation-intensive operations.
A SoC integrates a processor, memory modules, I/O peripherals, and custom hardware accelerators into a single chip.
We will construct several SoCs containing a Xilinx MicroBlaze soft-core processor, memory-mapped I/O subsystem that can incorporate custom I/O cores, ....

## Slide 20: Hardware-Software Co-Design
The FPGA technology allows us to tailor the processor, select only the needed I/O peripherals, create a custom I/O interface, and develop specialized hardware accelerators for computation-intensive tasks.
Both the hardware and software can be customized to match specific needs.
The methodology of exploiting the trade-offs between hardware and software and developing and integrating them concurrently is referred to as hardware-software co-design.

## Slide 21: Development Flow of SoC
  Partition the tasks to software routines and hardware accelerators
  Design user custom cores if needed
  Develop the hardware
  Develop the software
  Implement the hardware and software and perform testing.

## Slide 22: Final Remarks
At the end of this lecture you should be able to:
  Describe the main features of reconfigurable computing
  Outline a typical FPGA architecture
  Know difference between FPGA and PSoC
  Identify the main steps of FPGA design flow
  Define software-hardware co-design
To do:
  Install Xilinx Vitis 2020.2